Georg Fisher Type 375 Ball Valve – Engineering Specification

1.0 Summary

The product specified in this document is for Type 375 Ball Valve from Georg Fischer.

2.0 Specification and Certifications

The valve is to meet ASTM standards for PVC and CPVC materials. Flanged versions of the 375 valve shall meet the ANSI B16.5 150 lb standard. PVC versions of the Type 375 shall be NSF-61 approved for drinking water applications. Polypropylene versions shall be FDA CFR 21 177.1520 and USP 25 Class VI (physiological non-toxic) compliant. Polypropylene 375 valves will be in accordance with EN ISO 15494 specification.

2.1 Temperature

The 375 ball valves are rated for:

232 PSI for sizes 3/8” to 4” in PVC socket at 72°F

232 PSI for sizes 3/8” to 4” in CPVC socket at 72°F

150 PSI for sizes 3/8” to 4” in Polypropylene at 72°F

150 PSI for sizes 3/8” to 4” in all materials flanged or threaded at 72°F

2.2 Materials

The 375 valve body shall be constructed of PVC, CPVC, or Polypropylene. Seats are made of PTFE. Seals shall be made of FPM or EPDM.

2.3 Function

The 375 valve shall have a blow out proof stem with double o-rings. Valve seat carrier shall be adjustable. All PTFE seats shall have backing o-rings. The handle shall include in its design an integrated tool for removal of the union bush.

3.0 Approved Manufacturer

Approved manufacturer is Georg Fischer with no equal.