Specification For Paddlewheel Flow Sensor

- Sensor shall be capable of sensing flow in either direction ( bi-directional).

- The paddlewheel insertion flow sensor shall generate an electrical signal proportional flow velocity from a range of 0.3-20 feet per second.

- The sensor shall be inserted at the correct depth and there shall be a fully developed flow profile.  Linearity of the output signal shall be ±1% of full range, with a repeatability of ±0.5% of full range.

- The sensor shall not create a pressure drop of >1 psi at any flow rate.

- Two optional sensor lengths shall allow the flow sensor to install into a flow installation fitting.  Optional sensor lengths will allow insertion in pipes from 0.5 to 8 inches.

- The sensor body materials shall be glass-filled polypropylene (black) or, PVDF (natural).

- The electrometric seals shall be FPM-Viton® (standard) with optional EPDM or FFPM-Kalrez®.

- Rotor pins shall be Titanium (standard for PP), Hastelloy-C or PVDF (standard for PVDF), with optional ceramic, Tantalum, or stainless steel.

- Rotor material shall be black PVDF (standard for PP) or natural PVDF (standard for PVDF) with optional Tefzel® with or without Fluoraloy G ® sleeve.

- Sensor shall have integral mount electronics capable of 4-20 mA or, Digital (S3L)or, Flow switch, or pump pulser output.

- The flow sensor shall be a Georg Fischer Signet model 2537 or equal.